## Slide 1: Grid generation for SCHISM with SMS

## Slide 2: Overview of The GG process
Know your domain and target physics
Understand SCHISM numerics
  Usually it’s easy to get ‘reasonable’ results without much effort with GG
  You cannot take full advantage of SCHISM features unless you understand its physics and numerics
Elevation and contour data preparation
Digitize or determine boundary (ideally as shape files from Arc)
Import and refine conceptual model
  Identify critical features/contours
  Identify resolution/density
  Create polygons and patch/pave locations
  Generate the mesh
  Populate mesh elevations (depths)
Mesh quality and bathymetric metrics
Performance and accuracy metrics
Clip mesh as necessary for subdomains of interest

## Slide 3: (Ocean)-Bay-Delta
San
Francisco
San Diego
Redding
Los Angeles
San
Francisco
Delta
  Confluence of Sacramento and San Joaquin Rivers
  47% of California’s runoff passes through Delta

## Slide 4: SCHISM Bay-Delta and Bay Subdomain
Bay SCHISM
Bay-Delta SCHISM:
~180,000 nodes
~360,000 elements
Notes: This kind of clipping is now partially automated by scripts, so that when you update the full mesh all the subdomains can be automated
Delta coming soon

## Slide 5
South Delta Temporary Barriers
Clifton Court Forebay
Union Island
Roberts
Island
Jones Tract
Fabian Tract
Head of Old River
Middle River
Grant Line Canal
Old River at Tracy
Stockton
●

## Slide 6: Delta
Channelized, levees
Levees and “islands”
3D challenges beyond estuary processes
Extensive tidal influence

## Slide 7: Estuary Transport (3D)

## Slide 8: Shear Dispersion
From REALM,
An adaptive mesh code
Notes: This animation is from an adaptive mesh model (REALM) that illustrates how different resolutions look in a channel. The simulation shows the transport of a fictitious tracer and were designed to illustrate mixing. If you play it you can find moments when the effects of shear dispersion (fast in the middle, slow at sides) is very obvious. The larger grid cells at the top will miss this mixing because they don’t resolve the velocity and concentration differences over the channel. The finest cells are 16 times smaller and are probably overkill for this part of the Sacramento. 4-8 seems just about right.
Our goal with SCHISM is to be 1) medium resolution and 2) global. For important channels we use the length scale of shear dispersion to guide resolution in the horizontal direction. For smaller channels that contribute less to global accuracy, we sometimes elect to underresolve mixing details.

## Slide 9: Tools
Recommend SMS using “conceptual maps”
  Good advantage of terrain
  Patch/pave comparison
  Bugs, high level of manual work
Triangle is a good free product
  Driven mostly by exterior (2D shore)
Janet: expensive, orthogonality not needed
DistMesh: Beautiful introduction to density functions, curvature. Not all the good stuff is in the software.
Holleman et al 2013: Flow-aligned mesh and numerical diffusion, but orthogonal

## Slide 10: SMS Resources
SMS/Aquaveo website
Todd Wood Masters Thesis:
  Can be viewed from wiki (www.schism.wiki)
  Very good step-by-step
  Honest account of debugging such as “bisection” to find bad spots

## Slide 11: General rules
Unlike explicit models, you’ll find G.G. for SCHISM is more ‘intuitive’ and ‘freer’
  Implicit model allows you to focus on physics instead of numerics (CFL…)
  You are freer to resolve important features without worrying about cost/instability
  SCHISM is not picky about grid quality (except for quads); however, grid quality pays off for accuracy especially for baroclinic applications
  G.G. for baroclinic applications requires more effort (often an iterative process): establishing a good workflow is essential

## Slide 12: SMS Conceptual Model

## Slide 13: DEM preparation: pre-filtering bathymetry
Unresolved features may be eliminated
  eliminates lunar landscape undulations on mudflats
  level set or active contour methods (e.g. Malladi and Sethian): contours conservatively straighten
  California DWR has python code smooth_contour.py for small regions
  This is mainly to assist in the arc creation, less for actual interpolation of depths

## Slide 14
Liberty Island Smoothing:
Malladi and Sethian
Min-max curvature flow

## Slide 15: Wetting and Drying in the Frontal Direction is Costly (side shores are fine)
Undulating channel

## Slide 16: Generating Contour Shapefiles
ArcGIS allows graphical cleaning
GDAL (gdal_contour) is free and good for quick manipulation on-the-fly
SMS sister product WMS has some contour tools
All use bilinear interpolation
Note that SMS < 11.1 has a georeferencing mistake for contours (cell- vs vertex-centered)
Python shapefile library very useful for exporting arcs based on calculations in (x,y)

## Slide 17: Visualizing Contours
SMS has very limited memory
You can use a coarse tin or DEM for conceptual visualization or on small domains
clip_dem.py allows tailored geographical information

## Slide 18: Cleaning
Snapping vertices
Intersecting arcs
Dangling arcs
Mixed feelings about them all

## Slide 19: Magic Contours
Foot/top of slope, thalweg
Shoreline and probable “real” water levels
Flooding and mudflats
Key features (jetty, breakwater…)
TVD (h_tvd) and other algorithm switches
Depths used in friction and other user threshold choices

## Slide 20
h_tvd = 5m,
Water elev ~ 0.5m
so -4.0 NAVD contour mostly non-TVD
Channel
Shoal
Tidal range
Ship channel
Skew elements

## Slide 21: Choose Connected Contours
Changing from -2 to -3m increases connectivity
No need to be religious about following contours exactly
Well resolved without help

## Slide 22: Choose Smoother Deep Contours

## Slide 23: Stick with the center
Ignores inner channel
Follows inner channel without help
Inner channel delineated

## Slide 24: Grid Density
Need guidance from inverse CFL>0.4
  Start from a lowest expected Dt
  Use CFL>0.4 to back calculate the coarsest Dx at a given depth
Deeper regions generally coarser than shallows but not always (compare this with explicit models which are constrained by CFL)
  Often channel needs to be resolved for tracer transport
Curvature should be resolved:
  2D: bend in shorelines
  3D: changes in slope (vertical grid plays a role)
Width of features (sills, beaches, channels)
  Skeletonization algorithms (see Per-Olof Persson dissertation)

## Slide 25: Control Grid Density In SMS
Density-based paving
Shore resolution propagates in
Refinement nodes (node in map tool) can enforce local resolution (but may produce skew elements)

## Slide 26: Wetting and Drying
Element-based designation
  Based on node elevations
  All 3 wet => wet element
  No partial wet/dry
Velocities calculated on edges of wet elements

## Slide 27
Always wet
Clogged
Clogged or narrow
Mildly inaccurate: wrong contour?
Robust!!
With SCHISM you can faithfully represent channels (and other features), thru good choices of horizontal and vertical grids
In estuarine and near-shore applications, faithful representation of bathymetry and features is the right approach, as opposed to artificial manipulation of bathymetry

## Slide 28: Patching and Paving
Patch
Pave

## Slide 29: Mesh Types (Patch vs Paving)

## Slide 30
Bias easier to “undo” here

## Slide 31: Patch vs Pave
Pave:
Recommended for quality grids on large, well-resolved water bodies
Works well when polygon is big and wide compared to arc nodes
Most robust of all methods

## Slide 33: (Adaptive) Coon’s Patch
Quasi-structured grid block
Force mesh to be n-elements wide
Arbitrary anisotropy (3:1 or 4:1 common)
Follow the channel!!! Don’t round corners
Patch (Adaptive Coon’s Patch)
Pave (advancing front)

## Slide 34
Hydraulic Structures
1
2
Q
“Block”
Faces
1
2
3
4
5
5’
4’
3’
2’
1’
1-1’ etc are node pairs

## Slide 35: Dovetailing Patch and Pave*
*These ideas not unique to patch/pave

## Slide 36: Populating Elevations
Big problem again … SMS doesn’t hold the data gracefully
Have heard of people doing it in stages
Can use stacked_dem_fill.py, which:
  Populates with correct georeference
  Matches contours
  Uses prioritized DEMs
  Gives some warnings

## Slide 37: Metrics
Volumetric error (actually, average height)
  Patterns can be systematic
Face/edge aperture or area
Storage area
Skew: SCHISM very tolerant, but good to look (if you use xmgredit5, try skewness of 14)
Need to use quality quads (xmgredit5: angle ratio >0.5)
Area change: SCHISM very tolerant, but good to look
Slope: PGE issue usually not a problem (vgrid plays a role also)
Local error: Richardson extrapolation
  Painful without tools
TVD2 and sub-cycling measures
Eddying regime requires more uniform and higher-quality grid to avoid distortion of eddy dynamics
CFL (>0.4) and subcycling issues
  Xmgredit5 can easily check CFL for you
  Dimensionless wave number may also need to be looked at

## Slide 38: Bathymetry/Volume Matching

## Slide 39: TVD tuning
(Vertically) implicit TVD2 alleviated much of the pain
Use tvd_analyze.pl (we modify it to accumulate offenders over time)
Create a prop file and visualize
There is also a “hidden” dtbe visualization option

## Slide 41: Automatic regrid/subgrid
…it’s generally easier (and quicker) to regrid the whole grid

## Slide 42: Common Ad Hoc Fixup Steps
Deepening of boundary depths to prevent open boundary drying
There is a fancier approach to preserve the original depth…
In gredit, create a region and depth=max(depth,3)

## Slide 43: Conclusions
SMS is an adequate tool for non-ortho grids
Good grid generation resolves flow/bathy features faithfully
  Some finer scales ignored if not resolved
  Implicit model provides you with more freedom for resolution
Shape functions and wet-dry rules; understand the physics and numerics!
You can’t work on this stuff unless you can fix-test-fix-test
  So front-end on node-based inputs (see BayDeltaSCHISM)
IMPORTANT: always start from an estimate of smallest Dt you anticipate for the application and use CFL>0.4 to back-calculate the coarsest resolution at each depth
  If you somehow decide to reduce Dt later, you may have to refine the grid
  As a rough guide, Dt=100-450s for b-tropic, 100-200s for b-clinic applications (however, smaller Dt may be needed for some extreme cases)