## Slide 1: Mesh generation for SCHISM with SMS Joseph Zhang, VIMS Eli Ateljevich, DWR

## Slide 2: Grids
Structured grid
Dx
Dy
straightforward (except for curvilinear grids)
Hard to locally refine/adapt

## Slide 3: Grids
Unstructured grid
not straightforward (needs tools)
Flexible

## Slide 4: Know the rules!

## Slide 5: Good or bad mesh?
It depends…

## Slide 6
What’s the purpose of mesh anyway?
Mesh serves the purpose of resolving relevant processes
So skill assessment (quantitative/qualitative) is the ultimate criterion for ‘good/bad’ mesh
It’s a common mistake in UG models to over-emphasize the appearance of meshes (aka mesh quality)
  Smooth looking mesh
  Ugly mesh (skew elements etc)
  As long as it captures the underlying bathymetry…
  A very useful error metric is therefore the area/volume errors in mesh vis-à-vis DEM (bathymetry)

## Slide 7
Three guiding principles for in silico oceanography
To debunk the myth that coastal modeling inherently lacks rigor, we propose:
Principle #1: Bathymetry is a first order forcing in coastal domains
  Hence, observation-based DEM data should not be smoothed or otherwise manipulated beyond the resolution of the numerical grid
Principle #2: Oceanographic processes are driven across multiple scales
  Hence, grids must be as high resolution and extend over as large a domain as required by the processes and known forcing (and allowed by computational limits). This includes some ultra localized processes (e.g., small-scale shears)
Principle #3: Assessment should focus on processes
  Hence, traditional quantitative error metrics, while useful, are not a substitute for feature-based metrics and should not distract or mislead high-fidelity representation of processes
  Go beyond RMSE…
Zhang et al. (Ocean Modelling SI)

## Slide 8: The good news and bad news
Bad news
  UG mesh generation is often a laborious and iterative process
  Steepest part of the learning curve for UG models
  This is especially true for very large meshes: a common source of frustration with SMS – important to build confidence gradually
Good news
  SCHISM is not picky about mesh quality; at least won’t blow up easily
  Once you master the M.G., the rest of the model setup is more straightforward
A few ways to blow up the model
  Bad quality quads: split them to get pair of triangles using fix_bad_quads.f90
  Completely blocking the water flow, e.g., by under-resolving the main channel => noise
  Flow boundary entirely dry : a few ways around this
  Momentum dissipation too low (parameter choice)

## Slide 9: Mesh generation tools
We use SMS via “conceptual maps”
  + Good advantage of terrain maps
  + Patch (quads)/pave (triangles) comparison
  - High level of manual work (more control)
Triangle is a good free product: underpins many tools
Janet: expensive, orthogonality not needed
DistMesh: Beautiful introduction to density functions, curvature. Prototype only.
STOMEL (Holleman et al 2013): Flow-aligned mesh for less numerical diffusion, but orthogonality not needed
GMESH: freeware and has been incorporated into other packages
JIGSAW: recent addition that is gaining popularity. Mostly geared toward generating good-quality (good-looking) meshes (e.g. orthogonal)

## Slide 10: SMS Resources
SMS/Aquaveo website
Todd Wood Masters Thesis:
  Can be viewed from wiki (www.schism.wiki)
  Very good step-by-step
  Honest account of debugging such as “bisection” to find bad spots

## Slide 11: Tension between model and mesh
Tension between model and mesh has been a constant theme since the birth of UG model
  Conventional wisdom: mesh generator should accommodate models (aka: kick the ball to mesh generator)
  SCHISM philosophy: model should be able to accommodate any reasonable mesh, regardless of quality
    You only need to improve quality in areas of importance
mesh
model
Typical meshes used by other models
Typical meshes used by SCHISM
-

## Slide 12: Overview of MG process
Know your domain and target physics: mesh serves at the pleasure of physics
Understand SCHISM numerics
  Usually it’s easy to get ‘reasonable’ results without much effort
  You cannot take full advantage of SCHISM features unless you understand its physics and numerics
Digital elevation (terrain info) and contour (isobaths) data preparation (for feature detection)
Digitize or determine boundary (e.g., shape files from ArcGIS)
Create and refine conceptual model (SMS “maps”)
  Identify critical features/contours: channels, channels, channels…. (this is one aspect of SCHISM that differs from other models)
  Identify resolution (mesh density)
  Create polygons and meshing algorithms (patch/pave)
  Generate the mesh
  Populate mesh depths: linear interpolation (no smoothing, no manipulation)
Mesh quality and bathymetric metrics
  Eddying regime
  Performance and accuracy metrics (model tuning)

## Slide 13: Overview of SCHISM calibration
Calibration of model often involves remeshing
  When better DEMs become available (other models: reload)
  Need to locally edit an area
  Need to alleviate performance bottlenecks (efficiency)
Therefore, prepare upfront an iterative workflow that is reproducible
  Remember mesh is the most powerful weapon for UG models!
  Remeshing should be your normal routine
Mesh
Model
DEM

## Slide 14: Download and open bay_delta24.sms to follow the lecture
rsync -az yinglong@bora.sciclone.wm.edu:/sciclone/home/yinglong/DISKS/vims20/MSCI602/RUN01c .

## Slide 15: (Ocean)-Bay-Delta
San
Francisco
San Diego
Redding
Los Angeles
San
Francisco
Delta
  Confluence of Sacramento and San Joaquin Rivers
  47% of California’s runoff passes through Delta

## Slide 16: Delta
Channelized, levees
Levees and “islands”
3D challenges beyond estuary processes
Extensive tidal influence

## Slide 17: SMS Conceptual Model
Projection/unit
Nodes, vertices, arcs and polygons
DEM

## Slide 18: SMS Conceptual Model
Nodes, vertices, arcs and polygons
Nodes
Vertices
Feature nodes
Arcs
Polygons
Nodes: used mostly to delineate arcs (exception: refine nodes); fixed in place
Vertices: interior points of arcs, used to define resolution
  Will move when you adjust resolution
Arcs: lines consisting of nodes and vertices, used to form polygons
Polygons: collection of arcs for an enclosed area

## Slide 19: DEM (Digital Elevation Model)
DEMs serve as the foundation for mesh generation: mesh serves at the pleasure of DEMs
Imageries can help, but DEMs decide the final depths in mesh
  Inconsistency between the two is an issue
Types of DEMs
  Raster (regular grid): most common and simplest
  TIN (irregular grid or UG): tinnode_west* etc
TIN
Raster (.asc, geotif etc)
Vertical datum (reference level): NAVD88 is common (MSL, MLLW,…)​
  For models, we need a starting surface elevation ('0'), which corresponds to fluid at rest​

## Slide 20
Now turn on the display for DEM contours
We’ll need it to draw arcs

## Slide 21: Magic Contours from DEM
Foot/top of channel slope, thalweg
High-gradient zone in DEM for ‘features’ (e.g. shelf break)
Shoreline and probable “real” water levels (for initialization)
  Imagery can be used as a guide
  No need to be super precise (it’s moving!)
Any other important features (jetty, breakwater…) that may impact simulated processes
20m
thalweg
top
Foot

## Slide 22: Vertical datum
Shoreline/MSL is at 1m NAVD88
In this area, NAVD88 is ~1m below MSL
Adjust magic contours due to datum differences
Make sure contours are in equal interval (for features ID)

## Slide 23: Features
Channel
Shoal
Tidal range
Ship channel
Skew elements
Delineate channels and other features in the SMS map based on best DEMs
Steep bed slope Proximity of arcs skew elements (mostly fine)
Channels are more naturally represented with patches (quads)
Try not to over-constrain (which leads to very skew elements)

## Slide 24: Patching and Paving
Patch
Pave
Patches mostly consist of quads, but triangles are necessary for transition or sharp turns
Paving consists of only triangles

## Slide 25: Cleaning & build polygons
Cleaning
Snapping vertices
Intersecting arcs
Dangling arcs
Default tolerances usually work fine
Always clean the map before build
Build polygons: open polygons won’t be built

## Slide 26: Quiz
What's the first step in SCHISM modeling?
Get mesh from another model
Generate a new mesh
Compile DEM

## Slide 27: Quiz
Starting point of mesh generation is:
Imagery
Mesh from another model
DEM
All of the above
What are the two types of DEM formats?
How do we judge if a mesh is good or not?

## Slide 28: Quiz
2D stands for…
DEM, DEM
3D stands for…
DEM, DEM, DEM
What’s the most important features to capture in meshgen?
How should we mesh the channel?

## Slide 29: Mesh Types (Patch vs Paving)
Select polygon(s) to define meshing method

## Slide 30
Make sure there are only 4 corner nodes (merge/split some if necessary)
Preview
Note the mesh resolution in the cross-channel direction

## Slide 31: Paving channel
Select polygon  paving
Note the variably resolved cross-channel direction (compared to patch)

## Slide 32: Patch vs Pave
Pave:
Recommended for quality grids on large water bodies
Works well when polygon is big and wide compared to arc nodes
+ Most robust of all methods
Resolution harder to control in the interior (especially for elongated shapes): constant/scalar paving can remedy a bit

## Slide 33: (Adaptive) Coon’s Patch
Quasi-structured grid block
Force mesh to be n-elements wide (try to match on opposite boundaries)
Arbitrary anisotropy (3:1 to 5:1 common)
Can follow curved channel (up to a limit of curvature)
+ Easier to control cross-channel resolution; great for elongated areas
- Not flexible enough to fit complex geometry
Patch (Adaptive Coon’s Patch)
Pave (advancing front)

## Slide 34: Delineate features: choose connected contours
SMS prefers enclosed polygons
Changing from -2 to -3m increases connectivity
No need to be religious about following contours exactly
Patches (quads) require more regular shape
Depend on calibration needs
Well resolved without help
SMS is in most cases ‘predictable’
Try to ‘anticipate’ the final mesh as you go when you get enough experience
Guess what’d happen here?

## Slide 35: Choose Smoother Deep Contours
…to accommodate quads/patch
Sometimes, need to ‘cut corners’ to properly form patch
patch
pave

## Slide 36: Prioritize channels
Ignores inner channel because cross-channel resolution is fine enough
Follows inner channel only
Inner channel delineated
Deeper channels are where interesting processes occur (high gradients etc)
Shoals are of lesser importance
Options to form channels/patches…
Notes: Right most arcs: have choice on whether to delineate both channel and boundary.

## Slide 37: Mesh Resolution
Redistribute vertices of an arc
  Beware the unit (meters vs degrees)
Need guidance from inverse
  |u|: flow velocity
  : wave speed
  , : time step, mesh resolution
  M.G. starts from a smallest expected Dt (e.g., 100s)
  Use CFL>0.4 to back-calculate the coarsest Dx at a given depth
  Contrast to explicit models (CFL<1)
  Use xmgredit5 to check (in projection, not in lon/lat)
    Use ~yinglong/bin/cpp to convert lon/lat (select a center lon/lat of projection)
: 1.e-5 degrees ~ 1m

## Slide 38
Dt=100s (expected minimum*)
Remember to refine mesh if for some reason you have to reduce Dt below 100s
Small patches of violation is fine especially near shoreline; avoid it in open area
Mesh resolution Guide
Violation of CFL>0.4
Fine here

## Slide 39: Mesh Resolution
Deeper regions generally coarser than shallows but not always (compare this with explicit models which are constrained by CFL)
  Often channel needs to be resolved for tracer transport
Curvature should be resolved:
  2D: bend in channel
  3D: changes in slope (vertical grid plays a role)

## Slide 40: Interior Mesh Density with Paving
Density-based paving
Shore resolution propagates in
Refinement nodes (node in map tool) can enforce local resolution (but may produce skew elements if very constrained)
Density paving (constant or scalar) as alternatives: may not work for complex polygons
Other options to control interior resolution?

## Slide 41: Wetting and Drying in SCHISM
Element-based wet/dry
  Based on node elevations
  All 3|4 wet => wet element
  No partial wet/dry
Velocities calculated on edges of wet elements
Ensure at least 1 row of ‘always-wet’ elements to allow flow to go thru
  Account for tidal motion

## Slide 42
Always wet
Clogged
Clogged or narrow
Mildly inaccurate: wrong contour?
Robust!!
With SCHISM you can faithfully represent channels (and other features), thru good choices of horizontal and vertical grids
In estuarine and coastal applications, faithful representation of bathymetry and features is key, as opposed to artificial manipulation of bathymetry

## Slide 43: Post meshing
Remove disjoint nodes
Renumber nodes
  Create a nodestring first where the renumbering starts
  This reduces bandwidth of matrix, but more importantly, forces SMS to check mesh integrity
Save mesh as .2dm
Transfer to Sciclone and convert .2dm to .gr3 using:
  /sciclone/home/yinglong/git/schism/src/Utility/SMS/2dm2gr3_m2m.pl

## Slide 44: Post Meshing Check: mesh validity
Examples of illegal meshes for SCHISM
Overlapping (non-conformal): rare occurrence
Negative/zero elements: element's nodes numbering must follow counter-clockwise direction
Pinched nodes: any boundary node must be neighbored by exactly 2 other boundary nodes
Non-conformal
Pinched node
counter-clockwise

## Slide 45: Post Meshing Fix-up: bad quads
Quad quality is required as it’d defeat the intended purpose
Quality is measured as the ratio between min/max interior angle >=0.5
Always use the pre-proc ~yinglong/bin/fix_bad_quads

## Slide 46: Post Meshing Fix-up: small or skew elements
Use gredit to ID these (RUN01d)
  Local relaxation to alleviate constraints in connectivity: move node, swap edges, coarsening

## Slide 47: Loading from DEMs
Can do this inside SMS, but memory consumption is an issue
Use efficient scripts (even parallel)
  Basically go thru all DEM tiles and load
  Must prioritize higher-quality DEM tiles by loading them after lower-quality DEMs
No smoothing/manipulation needed for SCHISM! Linear interpolation is sufficient
dems={‘bad1’, ‘bad2’,…, ‘better1’,..,’best1’,’best2’,…}
bad1
bad2
bad3
better1
better2
better3
best1

## Slide 48: Post Meshing Fix-up: flow boundary
Deepening of flow boundary to prevent it from becoming completely dry
  Cover a few rows of elements near that boundary
  Use point sources as an alternative
In gredit, create a region and depth=max(depth,3)

## Slide 49: Post Meshing Check: channel connectivity
Round-off errors in contour extraction
Human errors
Ensure major channels are not blocked at any location
  Single point of failure (blockage) can block the channel flow
  Recall the wet/dry rule in SCHISM: at least one element should be always wet to allow the flow to go thru
    Need to factor in tides, so be conservative in your arc design to favor the ‘wet’ portion

## Slide 50: Post Meshing Check: inverse CFL
If you follow the table in mesh generation, this should not be an issue
In gredit, set a min depth of 0.1 before checking
  This is because , and the wave speed is undefined in shallow/dry areas, where |u| is dominant (~1m/s)
  In gredit, |u| is not included in

## Slide 51: Open and land boundary segments
With gredit, generate all open segments first followed by land segments
A shortcut if your open segments do not change much during mesh revision
  Using a bp input

## Slide 52: Summary
We use SMS to generate generic unstructured meshes
Good mesh generation resolves flow/bathy features faithfully
  Some finer features may be ignored if not important for your study
Shape functions and wet-dry rules; understand the physics and numerics
Channels, channels, channels…
You can’t work on this stuff unless you can fix-test-fix-test
IMPORTANT: always start from an estimate of smallest Dt you anticipate for the application and use CFL>0.4 to back-calculate the coarsest resolution at each depth
  If you somehow decide to reduce Dt later, you may have to refine the mesh
  Conversely, if you refine the mesh, you do not need to reduce Dt
  As a rough guide, Dt=100-450s for barotropic, 100-200s for baroclinic applications (however, smaller Dt might be needed for some extreme cases)

## Slide 53: Summary
Unlike explicit models, you’ll find M.G. for SCHISM is more ‘intuitive’ and ‘freer’
  Implicit model allows you to focus on physics instead of numerics (CFL…)
  You are freer to resolve important features without worrying about cost/instability
  SCHISM is not picky about mesh quality (except for quads); however, mesh quality may pay off for accuracy in some critical regions
  M.G. for 3D baroclinic applications requires more effort (often an iterative process): establishing a good workflow is essential so you can easily repeat the process if needed

## Slide 54: Quiz
What’s the inverse CFL criterion for SCHISM?
What are some examples of illegal mesh?
What’s the correct order of loading DEM tiles?
What are things to pay attention to in meshing channels?