## Slide 1: Lab: Meshing a toy problem

## Slide 2
Sciclone setup
.cshrc*
Test gredit
Work on either /sciclone/data10 or schism10
To prepare for future classes:
Copy all files in my MSCI602 dir to your desktop and to your Sciclone dir
On Sciclone: rsync -aLz /sciclone/home/yinglong/DISKS/vims20/MSCI602 <your dir>
To desktop: rsync -aLz <your UID>@boara.sciclone.wm.edu:/sciclone/home/yinglong/DISKS/vims20/MSCI602 <your dir>
ctrl-z to push to background followed by bg
Install pylibs and pySCHISM

## Slide 3
A toy case for estuary-shelf model
R=150km
Estuary: 400km x 12 km
River: 40km x 1km
Depth (m)
Try to follow the dimensions shown here but it's OK to use your own
  Linear slopes used here
  River depth at boundary = 1m
  Estuary depths from –1m to 20m (channel)
  Shelf depths from 20m to 1km
Create two open segments: ocean and river
45km
3km
12km
Ocean bnd
z=0
20m

## Slide 4
Compile SCHISM package
Clone SCHISM github to your own dir (cf. Online manual)
git clone ...
cd into dir
git checkout tags/v5.11.0
cd cmake; mkdir build; cd build

## Slide 5: Lab: Meshing Delaware Bay

## Slide 6
Background
DE Bay is a typical estuary in Mid Atlantic Bay (read Whitney & Garvine 2006)
Main tributary is Delaware River: flow of ~100 to ~1000 m3/s
Meso-tidal estuary with a maintained/dredged shipping channel
Numerous smaller tributaries – typical of most estuarine systems: e.g., Schuylkill
Economically significant system: Philadelphia

## Slide 7
Your tasks
Based your understanding of the estuarine systems, generate a mesh for DE Bay
DEMs are in: /sciclone/home/yinglong/DISKS/vims20/MSCI602/RUN01b
  Set projection to WGS84 (geographic) - this is set automatically after you load geotifs below
  Use geotif for SMS; contours_-20to0m/ has shapefile for isobaths from –20 to 0 in interval of 2m
  Cut land boundary at ~10m above sea level to include some watershed
  Ocean boundary at the entrance
After a mesh is generated
  Create and cd into your working dir on Sciclone
  rsync -aLz /sciclone/home/yinglong/DISKS/vims20/MSCI602/RUN01b .
  Transfer your .2dm (Windows) to this dir (RUN01b)
  Convert .2dm to .gr3: ~yinglong/Scripts/2dm2gr3_m2m.pl 1 new.2dm new.gr3
  Visualize it with gredit
  Check negative/small/skew elements
  Fix bad quads: ~yinglong/bin/fix_bad_quads (tolerance of 0.5). The output is hgrid.gr3.new
  Rename hgrid.gr3.new as hgrid.old (mv hgrid.gr3.new hgrid.old). Make sure it's in lon/lat
  Load depths using load_dem.pl
  Check bathymetry against DEM! Especially channel connection
  Check CFL>0.4
  [xmgredit5] Generate open boundary: ocean, DE River as a minimum
  Fix flow open boundary (DE River) if necessary (set a min depth of 3m) to allow flow into the domain
  Append b.c. part to hgrid.gr3

## Slide 8
Homework #1
Finish DEB mesh
Submit SMS map and final hgrid.gr3 (with depths loaded and b.c. Part included)
  You can upload your files onto Sciclone for me to review (remember to set read permission), or upload them to 1Drive or G-drive
Due in 2 weeks