## Slide 1: LSC2 vertical grid system
Joseph Zhang

## Slide 2: Vertical grid: LSC2
z (m)
Degenerate prism

## Slide 3: LSC2 script: define transect(s)
Step 1: prepare transect(s) using gredit
You can combine as many transects as you want to get a comprehensive view of the vgrid
Depth (m)
Notes: Used CA_DWR/RUN84b

## Slide 4: LSC2 script: gen_vqs.f90
!m_vqs: # of master grids
m_vqs=9
dz_bot_min=0.1 !min. bottom layer thickness [m]
allocate(hsm(m_vqs),nv_vqs(m_vqs),a_vqs(m_vqs))
hsm=(/0.4,10.,50.,100.,2.e3,4.e3,6.e3,8.e3,1.1e4/) !.,2000.,1.1e4/)
nv_vqs=(/2,24,30,33,33,33,33,33,33/)
! nv_vqs(6)=nv_vqs(5)+4
! nv_vqs(7)=nv_vqs(6)+4
! nv_vqs(8)=nv_vqs(7)+5
if(m_vqs<2) then
write(*,*)'Check vgrid.in:',m_vqs
stop
endif
if(hsm(1)<0) stop 'hsm(1)<0'
do m=2,m_vqs
if(hsm(m)<=hsm(m-1)) then
write(*,*)'Check hsm:',m,hsm(m),hsm(m-1)
stop
endif
enddo !m
! Other consts.
! Stretching const. for the 1st master grid and also for depth <= hsm(1)
! |a_vqs0|<=1 (1: skew toward bottom; -1: toward surface; 0: no bias)
a_vqs0=0
Controls near bottom resolution (used to consolidation of near-bottom levels)
FORTRAN and mlab Scripts in /sciclone/home/yinglong/DISKS/vims20/MSCI602/RUN02a
# of master grids (depths)
Depths (ascending order; covers max depth)
# of levels for each master depth (same order)
Stretching constant for shallowest depth
Step 2: Define master depths and # of levels
Notes: Used CA_DWR/RUN84b

## Slide 5: LSC2 script: gen_vqs.f90
! Define master grids
do m=1,m_vqs
do k=1,nv_vqs(m)
sigma=(k-1.0)/(1.0-nv_vqs(m))
! Option 2: S
theta_b=0
if(m<=2) then
theta_f=1
else if(m==3) then
theta_f=2
else if(m==4) then
theta_f=3
else if(m==5) then
theta_f=6.2
else if(m==6) then
theta_f=6.6
else if(m==7) then
theta_f=7.0
else if(m==8) then
theta_f=7.3
else
theta_f=7.5
endif
cs=(1-theta_b)*sinh(theta_f*sigma)/sinh(theta_f)+ &
&theta_b*(tanh(theta_f*(sigma+0.5))-tanh(theta_f*0.5))/2/tanh(theta_f*0.5)
z_mas(k,m)=etal*(1+sigma)+hsm(1)*sigma+(hsm(m)-hsm(1))*cs
enddo !k
enddo !m
! Generate a master vgrid (z_mas)
etal=0 !used in master grid only; elev.
if(etal<=-hsm(1)) then
write(*,*)'elev<hsm:',etal
stop
endif
nvrt_m=nv_vqs(m_vqs)
print*, 'nvrt in master vgrid=',nvrt_m
allocate(z_mas(nvrt_m,m_vqs))
z_mas=-1.e5
Step 2: Define z-coordinates for each master grid/depth
Adjust qb and qf here
Notes: Used CA_DWR/RUN84b

## Slide 6: S-coordinates
* Note that S-transformation degenerates to s-transformation when h<hc
qb=0: resolve surface only
qb=1: resolve surface & bottom

## Slide 7: S-coordinates
qb=0.7: resolve surface and a zone above bottom

## Slide 8: LSC2 script: inspection & adjustment
Step 3: compile and run the script; viz the transect(s) with plot_VQS.m
Step 4: repeat Steps 2-3 if needed to achieve a desirable vgrid
Meters or degrees (from hgrid.gr3)
Gaps between different segments
Notes: Used CA_DWR/RUN84b

## Slide 9: LSC2: demo
Set theta_b=1 (resolve the bottom) and adjust theta_f’s
Use fewer master grids (degeneracy)
Change dz_bot_min (degeneracy)
To launch matlab:
qlogin -q matlab -t 100 1:x5672:ppn=1
(request here max 100 minutes)
module load matlab
Matlab –nosplash
On James:
qsub -X -I -l walltime=1:00:00 -l nodes=1:potomac:ppn=1 -q matlab
Notes: Used CA_DWR/RUN84b

## Slide 10: LSC2: tuning
Generally, the master grid and the final transect grid should be ‘pleasing to the eye’, with resolution applied where you wanted
  Use many transects to catch potential issues
  Usually resolve surface at the expense of bottom but…
Symptom #1: going against terrain
  Solution: adjust # of levels, stretching constants in master grids
Symptom #2: too many degenerate (shaved) cells near bottom
  Potential causes: too few # of master grids and large differences between adjacent master grids; dz_bot_min;
Master grid
Against terrain
Too many
degenerate prisms?
Too few # of master grids
Notes: Demo on using transect.bp (/sciclone/home10/yinglong/vims20/CA_DWR/RUN84d/Vgrid)

## Slide 11: Flexibility in LSC2: add Z layers near the bottom
LSC2 is highly customizable (like UG in the horiznotal)
One possibility is to specify z layers after certain depths to save cost (esp. in deep ocean)
!Last 3 master grids
z_mas(1:nv_vqs(5),6)=z_mas(1:nv_vqs(5),5)
z_mas(1:nv_vqs(5),7)=z_mas(1:nv_vqs(5),5)
z_mas(1:nv_vqs(5),8)=z_mas(1:nv_vqs(5),5)
z_mas(1+nv_vqs(5):nv_vqs(6),6)=(/-2400.,-2900.,-3500.,-4000./)
z_mas(1+nv_vqs(5):nv_vqs(7),7)=(/-2400.,-2900.,-3500.,-4000.,-4500.,-5000.,-5500.,-6.e3/)
z_mas(1+nv_vqs(5):nv_vqs(8),8)=(/-2400.,-2900.,-3500.,-4000.,-4500.,-5000.,-5500.,-6.e3,-7.e3,-8.e3,-9.e3,-1.e4,-1.1e4/)
Copy 5th master to 6th, 7th and 8th
Specify z coorindates directly
See RUN02a/gen_vqs_addZ.f90

## Slide 12: Flexibility in LSC2: region-based masters
Use multiple sets of master grids in different parts of domain
  Different sets are stitched together at ‘choke’ points
  Ensure smooth transition: different sets of master grids must match at the borders
Master grid #1
Master grid #2
The 2 master grids share same coordinates for h<=100m
Bosphorous Strait
Marmara Sea
Black Sea