## Slide 1: SCHISM calibration: some typical issues
Joseph Zhang

## Slide 2: Wet/dry in shallow region: 2D vs 3D
2D and 3D models react to the bottom friction very differently
2D model does not allow vertical shear, so large friction will slow down the flow
3D model allows large vertical shear large friction will create large shear & numerical noise!
3D model will work well with small friction
Best strategy: use LSC2 and 2DH in shallows

## Slide 3: Wet/dry in shallow region
# of levels
2D/3D transition
In 3D, the roughness formulation leads to large CD in shallow area - a recipe for disaster (and an artifact)
Limiting CD in the shallow helps: 3D model prefers smaller CD in shallows
  2D model can handle small or large CD
2D or 3D: make sure that channels are not 'blocked‘ by using at least 1 row of always-wet elements
Locally 2D configuration helps: use LSC2!
  Pay attention to 2D/3D transition: using a small friction there always works

## Slide 4
Blow up or strong instability
Tide+storm surge (Hurricane Isabel) simulation for Chesapeake Bay
2D is successful
3D has large velocity and noisy/large elevation
Changes from 2D to 3D: reasonable bottom roughness and vgrid.in
What went wrong?
2D
3D
Days
h
In param.nml:
itur=0
dfv0=1.e-6 !viscosity
dfh0=1.e-6 !diffusivity
You cannot master numerics without understanding physics!
Notes: Hint: dt, itur=0 with small viscosity, …

## Slide 5: Transport efficiency bottleneck; WENO dispersion
To alleviate bottleneck of the explicit horizontal advection solver
  Use tvd.prop and h_tvd, and/or
  Use ELM to limit max # of subcycling (max_subcyc)
Beware the combination of ELM and WENO as the latter has numerical dispersion
  Symptoms are usually easy to notice: high and persistent tracer gradients
  Caused by the high gradients brought in by ELM that exacerbate the numerical dispersion
  Not an issue between ELM and TVD/upwind
  Solution
    Use a sufficiently large max_subcyc (to limit the use of ELM)
    Make sure ‘WENO’ zone in tvd.prop has sufficient mesh quality
    Start with upwind in most nearshore areas, and gradually add WENO in tvd.prop (upwind/ELM combination does not pose any issue)
Notes: Used CA_DWR/RUN84b

## Slide 6: Transport efficiency bottleneck: WENO dispersion
Poorly resolved channel (this leaves WENO zone in close contact with potential ELM zone)
Poorly resolved but also bad quality
Notes: Used CA_DWR/RUN84b

## Slide 7
Savannah River tides
Tides are damped in Savannah River system
Notes: RUN06a_JZ

## Slide 8
Savannah River: bathymetry
Used BlueTopo as DEM, which has a disrupted channel upstream
Imposed min depth of 4m upstream to get continuous channel
However, it turned out the tidal reflected by the shallow upstream channel is crucial for the tidal amplitude!
Be careful when you manipulate the depths!
Imposed a min depth of 1m instead
Bathymetry (m)
Notes: RUN06a_JZ

## Slide 9
Savannah River tides: original BlueTopo
Tides are improved!
DEM, DEM, DEM…
Ask for this info when working with other models before looking at their results!
Notes: RUN06a_JZ

## Slide 10
Hydrologic flow
River in/out of domain creates source/sink pairs in close proximity
This pathological configuration can lead to large positive/negative elevations
Hydrologic flow is very complex
Sensitive to topography
Notes: Hint: dt, itur=0 with small viscosity, …

## Slide 11
Hydrologic flow
Steep slopes on coarse resolution can lead to poorly resolved watershed
This can generate ‘pulses’ of high-speed flow and strange tracer patterns
Notes: Hint: dt, itur=0 with small viscosity, …

## Slide 12
Hydrologic flow
Inflow is stuck on low ground (‘bowl’) as it’s blocked by ‘mountains’
Refining mesh helps
Notes: Hint: dt, itur=0 with small viscosity, …

## Slide 13
Hydrologic flow
Poorly resolved channel leads to ventilation issue
Water will have trouble coming out smoothly
Consider refining here
Notes: Hint: dt, itur=0 with small viscosity, …

## Slide 14: The case of under-resolution in eddying regime
u
u
1
2
Under-resolution occurs frequently in areas of steep slopes, mostly to save cost in areas of no significant interest
In general, under-resolution in the horizontal dimension should be matched with an under-resolution in the vertical, often taking advantage of many degenerate prisms near the bottom. This reduces PGE
Time step may be reduced to stabilize the momentum over the steep slopes (useful for submesoscale processes)
  Remember to recheck CFL>0.4 if you reduce time step!
Florida

## Slide 15: Transition between eddying and non-eddying regime
Sharp mesh transition, with insufficient dissipation
Smooth transition (no additional dissipation)
Sharp resolution change in transitional regime triggered artificial accumulation of energy
Two solutions
  Make sure the mesh transition is smooth
  If non-smooth transition must be used, add extra numerical dissipation in shapiro.gr3 or use niter_shap
Filter strength

## Slide 16: A few ways to blow up the model
Violation of inverse CFL criterion in open water areas
Blocked main channel
Completely dry open boundary segment with imposed flow b.c.
Bad quality quads: always use the pre-proc script
Large CD in shallow regions with 3D cells
Improper parameter setting:
  indvel=ishapiro=ihorcon=0 (no dissipation)
  Inter subdomain back-tracking dimensions (s1_mxnbt, s2_mxnbt); increase these gradually for sharply transitioned meshes
Always visualize surface velocity in animation mode to find potential issues

## Slide 17: Summary

## Slide 18: SCHISM model …
Is an implicit model without mode splitting
Uses Galerkin FE formulation
Uses Eulerian-Lagrangian Method for advection
Numerical diffusion and dispersion are balanced and can be adjusted in different regimes
Therefore….
Large Dt is required for accuracy and convergence (CFL>0.4)
No mesh orthogonality is necessary – skew elements and sharp transition of resolution are tolerated, at least in non-eddying regime

## Slide 19: When generating a mesh for SCHISM…
Make sure major channels are resolved with at least 1 row of ‘always wet’ elements – no blockage of channel flow
Always keep the SMS map file and DEM sources and be willing to edit the mesh, as often the model results (and sometimes performance) depend on it
First estimate the smallest Dt you’d use, and then estimate the coarsest Dx at sample depths to ensure CFL>0.4
Resolving features is much easier with SCHISM – be game! Bathymetry smoothing is not necessary
Implicit TVD2 transport is very efficient, but horizontal transport is still explicit (and is the main bottleneck)
  Beware of mesh resolution in critical regions to avoid excessive sub-cycling
  Use upwind in areas of no stratification
Dt=100s

## Slide 20: When setting up SCHISM…
Always check the mesh first with a 2D model with ipre=1
Start from simple and then build up complexity
Examine surface velocity in animation mode to find potential issues
Start with time step of 150s
Avoid large CD in shallow areas in 3D regions (suggestion: start with 0.0025): polymorphism helps
Make sure open boundaries stay wet during simulation (or use source approach)
Negative river flow for inflow with open boundary approach; positive for inflow with source approach
Notes: B-tropic model; with const. forcing ….

## Slide 21: When calibrating SCHISM…
Remember the mesh is the single most important factor for accuracy – here lies the greatest strength and challenge of unstructured grids
Control the balance between numerical diffusion and dispersion (indvel, ihorcon…)
LSC2 grid is a very powerful tool (resembling unstructured grid in the vertical)
Transport solver performance may require some experience
Notes: B-tropic model; with const. forcing ….

## Slide 22: Get help
Remember you are not alone… ask question via mailing list
Help (and truth) is out there…
Happy UG modeling…