## Slide 1: Progress on 3D project
Wei Huang, Fei Ye, Joseph Zhang , Dan Yu and Karinna Nunez
Virginia Institute of Marine Science
03/10/2020

## Slide 2: Overview of progress
Assess NWM v2.0 products
Improve NWM coupling script: add an option to merge the source/sink pairs within a specified distance to avoid 'disappearing' flow
For 3D baroclinic runs, improve the efficiency of interpolating HYCOM outputs for I.C., B.C. and nudging files: 5 times faster, can be finished within 10 minutes
Revised grid in several regions to capture features in high-resolution DEMs to improve model skill
Preliminary results of two 3D baroclinic simulations of Hurricane Katrina
Worked on the subcycling issue in the transport solver to enhance the efficiency of 3D simulation
3 manuscripts drafted from current results
Preparing 3D baroclinic run for Hurricanes Harvey and Florence

## Slide 3: Assess NWM v2.0
NWM v2.0 has comparable results at most rivers
Seems to give less accurate flows for Atchafalaya and Mississippi River?

## Slide 4: Improving NWM coupling script
Added extra option to merge source/sink fluxes within a given distance
In this way, meandering rivers going into/out of elements within this given distance will be merged.
In the latest setup, sinks are merged with the nearby (< 4 km) sources

## Slide 5: Prepare input files for 3D baroclinic simulation
Revise rivers with large discharge and stations with large errors (Mississippi River, Rivers in Mobile Bay, Delaware distributes, and station near Wachapreague)
Fixed a few small elements to alleviate subcycling in the transport solver, and enhance the model’s efficiency.
Relieve a bottleneck in pre-proc: interpolation from HYCOM
  Revised scripts for interpolating HYCOM outputs onto I.C. and B.C. are more efficient: can be generated within 10 min, which is 5 times faster
  For example: Mississippi River, use larger along channel resolution for elements along Mississippi River

## Slide 6: Preliminary results for Hurricane Katrina (Uncalibrated 3D baroclinic simulation)

## Slide 7: Simulated surface temperature - signal of Katrina
Hurricane Katrina’s path
Simulated
Sea Surface Temperature (oC)

## Slide 8: Simulated surface velocity - signal of Katrina
Zoomed-in view on the Mississippi River
Simulated surface velocity (m/s)

## Slide 9: Grids in the Mississippi River
z (m)
Vertical grid
Mississippi River
Bathymetry (m)

## Slide 10: Discharge and elevation in the Mississippi River
Fresh water inputs from NWM (time-averaged around the Katrina period)
9188 m3/s
Mississippi River
Days from 2005-08-10
Discharge (m3/s)
There should probably be a second peak during the river flooding period
Simulation
ends
Hurricane Katrina
River flood
NWM Source locations, scaled by discharge
Elevation (m)

## Slide 11: Along-channel salinity distribution in the Mississippi River
Landfall of Katrina
Stratification before the storm
Salinity intrusion after the storm
downstream
upstream
z (m)
Along-channel distance (km)
Salinity (PSU)
Mississippi River
If the simulation extends to the river flooding period, salinity should be pushed seaward again.
Simulation ends before the river flooding period

## Slide 12: Simulated maximum elevation with/without NWM
With NWM
Without NWM

## Slide 13: Manuscript 1: Tidal Simulation Revisited
1Wei Huang, 1Y. Joseph Zhang, 1Fei Ye, 1Karinna Nunez 2Saeed Moghimi, and 2Edward Myers, 1Haocheng Yu,
1 Virginia Institute of Marine Science, College of William and Mary
2 NOAA National Ocean Service
Abstract: Accurate simulation of tides nearshore is necessary for any hydrodynamic model and a pre-requisite for other more complex processes. This study highlights the most important factor of simulating tides: the bathymetry. Main controls of tidal simulation are assessed: bottom friction, horizontal resolution/quality of model grid, quality of DEMs, high-order numerics and time step. The results show that the model can only perform well if high-quality DEMs are available and bathymetry is properly represented with locally high grid resolution, thus demonstrating the central role played by bathymetry in tidal simulation.

## Slide 14: Validation of major tidal constituents
stations that are highly uncertain due to low-quality DEMs
Wachapreague No high quality DEMs
Cedar Key, FL
stations
Tidal amplitude (m)
SCHISM
OBS

## Slide 15
Unable to fix Wachapreague station due to bad quality DEM
Simulated tides are severely under-estimated at this station
Setting bottom friction for the nearby region to be 0 improves the results but this choice is not defensible (prevalence of vegetations locally)
Resolving grid with higher resolution did not help
Real culprit: fake values in the high-resolution DEM

## Slide 16: Importance of resolving bathymetry based on high quality DEMs
Given that high resolution/quality DEMs are available in most areas, resolving grid to well represent bathymetry is found to be the most importance factor in improving model skill
Nantucket Island, MA
Chatham, Lydia Cove, MA
Resolved
Not resolved

## Slide 17: Conclusions for paper
Without good quality DEMs, adjusting friction may not always be able to compensate fully
Without good quality DEMs, high-order numerics or baroclinicity cannot make up for the deficiency*
Good quality DEMs yield accurate results only if the grid well resolves the bathymetry/geometry
Mesh quality plays a relatively minor role in SCHISM’s performance*
* more evidence is being gathered to support some of these conclusions

## Slide 18: Manuscript 2: Wind induced quasi-steady state balance for 12 coastal water bodies along east and south coast
1Wei Huang, 1Joseph Zhang, 1Fei Ye, 2Chunyan Li, 1Haocheng Yu, 1Karinna Nunez, 3Saeed Moghimi, and 3Edward Myers
1 Virginia Institute of Marine Science, College of William of Mary
2 Department of Oceanography and Coastal Science, School of Coast and Environment, Louisiana State University
3 NOAA National Ocean Service
Abstract: Quasi-steady state balance is an equilibrium state controlled by a simple first order linear equation between wind and pressure gradient. It was found in multiple water bodies along Louisiana coast including Lake Pontchartrain, Barataria Bay, Calcasieu Lake, and an Arctic lagoon: Elson lagoon. This paper checks 12 coastal water bodies along east and south coast of the continent of United States using SCHISM. The results indicate that quasi-steady state is fulfilled for all the 12 coastal water bodies. The accuracy of the quasi-steady equation depends greatly on the geometry/shape/opening of each system.

## Slide 19
Quasi-steady state balance is an equilibrium between pressure gradient and wind stress by the following equation
Take advantage of SCHISM’s creek-to-ocean, summit-to-sea capability
Apply quasi-steady state equation to 12 coastal water bodies

## Slide 20: Manuscript 3: Comparison of storm surge induced by multi-scale atmospheric systems
1Wei Huang, 1Y. Joseph Zhang, 1Fei Ye, 1Karinna Nunez 2Saeed Moghimi, and 2Edward Myers, 1Haocheng Yu,
1 Virginia Institute of Marine Science, College of William and Mary
2 NOAA National Ocean Service
Abstract: In Sep, 2011, Tropical storm Lee has great impact on Louisiana coast, which follows a few days after Hurricane Irene. Tropical storm Lee is unique in a sense that it combined with a strong cold front event, thus has significant impact on the coastal area. This manuscript aims to study the effect of different scale of atmospheric systems including cold front, tropical storm, and hurricane in 2011 on the hydrodynamics by 3D SCHISM model.

## Slide 21: Objectives: study the responses of hydrodynamic responses to different types of weather systems.

## Slide 22: Ongoing work
Add all remaining levees in lower Mississippi (Wei)
3D simulations and calibration of 4-5 hurricane events (Wei & Fei)
Efficient auto detection algorithm for thalwegs in watershed using ArcGIS Pro (Karinna)
Thanks!