## Slide 1: DEMs and New SCHISM Grid for East Coast and Gulf of Mexico
Wei Huang, Karinna Nunez, Dan Yu, Fei Ye, and Joseph Zhang
12/10/2019

## Slide 2: Summary of progress
Preparation of multiple DEMs from coarser to finer resolution
  Size issue is severe for SMS
  Used GIS to resample, split rasters, convert format (from .tif to .asc) and extract isobaths.
  All in NAVD88
Revised SCHISM grid for east coast + GoMX
  Resolved some barrier islands
  Added channels for major rivers (Missi.; Hudson; Ches Bay; DE Bay) and shipping channels in LA and TX Bays
Coupler to NWM streams using Fortran script

## Slide 3: DEMs from coarser to finer resolution
NOAA_CRM (3 arc-s, 90m)
https://maps.ngdc.noaa.gov/viewers/bathymetry/?layers=dem
Loading DEMs from NOAA CRM, ~90m resolution.

## Slide 4: DEMs: Coastal Digital Elevation Model (NOAA)
1 arc resolution
1/3 arc resolution

## Slide 5: DEMs: CUDEM (NOAA)
1/9 arc-s resolution
NOAA_CUDEM (1/9 arc-s, 3m, nav1983, navd 88)
https://maps.ngdc.noaa.gov/viewers/bathymetry/?layers=dem

## Slide 6: DEMs: USGS CONED
1-3 m resolution
USGS_CoNED (1m, nav1983, navd 88)
https://topotools.cr.usgs.gov/topobathy_viewer/

## Slide 7: Revised SCHISM grid
Adding arcs along barrier islands with resolution of 1500 m

## Slide 8: Revised SCHISM grid
Adding channels for major rivers using quads: Hudson River, Mobile Bay, Mississippi River, Atchafalaya River, Calcasieu Lake, Galveston Bay
New grid has 1.8 M nodes, 3.6 M elements

## Slide 9: Loading DEMs from coarser to finer resolution

## Slide 11: Coupling of NWM streams using Fortran script
How are the points along a NWM stream segment arranged? What is the direction of the flow or how to determine the direction of the flow?
We assume the points are arranged from upstream to downstream.

## Slide 12: TODO
Finalize the revised grid
Finalize the FORTRAN coupling script
2D calibration for Hurricane Irene
2D calibration for Hurricane Harvey