## Slide 1: Coupled hydrological-hydrodynamic large-scale simulation
Wei Huang, Y. Joseph Zhang, Fei Ye, Haocheng Yu, Karinna Nunez
Virginia Institute of Marine Science
Saeed Moghimi, and Edward Payson Myers
NOAA National Ocean Service

## Slide 2
Overview
SCHISM 3D modeling system
Model setup for Hurricane Irene: coupling to NWM
Grid generation
Challenges and success: bathymetry, bathymetry, bathymetry….
Summary
*Publications:
Zhang et al. (in press) Simulating compound flooding events in a hurricane, Ocean Dynamics.
Ye et al. (2020) Simulating storm surge and compound flooding events with a creek-to-ocean model: importance of baroclinic effects, Ocean Modelling, 145.
Notes: 0.5 min

## Slide 3
WRF
ESMF coupler
WWIII
ELCIRC-sub (street-level inundation)
Solves 3D Navier-Stokes equations in hydrostatic form with Boussinesq approximation
Galerkin finite-element and finite-volume approach: generic unstructured grids
  Semi-implicit time stepping: no mode splitting  large time step and no splitting errors
Eulerian-Lagrangian method (ELM) for momentum advection  efficiency & robustness
SCHISM: Semi-implicit Cross-scale Hydroscience Integrated System Model
  Mixed grids (tri-quads)
  Flexible LSC2 vertical grid
  Higher-order, monotone transport: TVD2; WENO3;
  Higher-order momentum advection (ELM with ELAD)
  ESMF ready
Unsmoothed bathymetry
Polymorphism
Resolution on demand (skew elements)
Robust seamless creek-to-ocean, Summit-to-Sea capability
SCHISM offers the capability of multi-scale physics/biology and
the following technological advantages:
… the goal is to minimize grid nesting as much as possible
Notes: 1.5 min

## Slide 4
Polymorphism
1
2
P
Q
R
A
B
Zhang et al. (2015)
A single grid mimics 1D/2DV/2DH/3D cells
Efficiency and flexibility
Shaved cells for bottom controlled processes
As a result, the underlying bathymetry can be accurately represented, including steep slopes
Notes: 1 min

## Slide 5
Un-smoothed bathymetry
USGS high-resolution DEM (NAVD88) (flat datum)
Explicitly representing NWM segments in the horizontal grid
Grid resolution: 2~7 km in the ocean; 50-200 m in the main channels; down to <20m in small streams
Terrain following vertical grid with varying number of layers (LSC2): 19 on average
3rd order transport scheme based on WENO
Ocean boundary forced by HYCOM
Hot start from HYCOM (with approximated salinity/temperature field inside the estuaries)
Atmospheric forcing from ECWMF (ERA)
Freshwater inflow inside Delaware Bay from NWM
Simulation period: 2011-7-27 ~ 2011-9-10 (50 days)
Time step: 150 seconds
Model setup: seamless creek-to-ocean
Delaware Bay (3D baroclinic): 759K nodes and 1,478K elements. 80x Real Time on 1440 cores of Pleiades (NASA)
East coast + Gulf of Mexico: 2.2 mil nodes
  The 2D model runs approximately 300 times faster than real time and can be efficiently conducted using as few as 500 cores
  Working on 3D model
Two major setups
Notes: 1 min

## Slide 6
The intersection points between NWM Segments and the SCHISM land boundary are determined.
NWM flows are directly injected at the intersection points
One-way coupling at the moment, from NWM to SCHISM
Coupling with NWM
NWM segments that
intersect the SCHISM
land boundary
SCHISM land
boundary
NWM segments
(a)
(b)
Sink discharge
Source discharge
Total source elements: 6835
Total sink elements: 1348
Notes: 1 min

## Slide 7: DE Bay setup: 3D baroclinic baseline
Brown color is dry land
SST (oC)
SSS
SST
river - noriver (m)
Elevations are generally well simulated, including compound surges in rivers
Baroclinicity is important during post-storm adjustment
Significant differences (~1m) appear in upper Bay and also near streams
Notes: 1.5 min

## Slide 8
Grid Generation
DEM preparation: >300 tiles
Major steps with SMS
  Resolve all major channels
  Patches are great way to resolve channels
NWM segments are explicitly incorporated
  Use GIS tools to clean up first
  Robustness of the model greatly helps: did not bother to clean up skew elements
Highly flexible to incorporate any small features: important for model skill locally
Hudson River
Lake Pontchartrain
Missi. R.
Flood levees are resolved!
Chesapeake
Mobile Bay
Galveston Bay
Delaware Bay
New York
Missi. R.
Notes: 1 min

## Slide 9
2D barotropic simulation during Hurricane Irene
M2 Tidal amplitude
Model skill at most stations are good.
Remaining issues: coarse DEMs, grid resolution at 2 stations in SC and VA.
Model results: Harmonic analysis
Notes: < 1 min

## Slide 10
Model results: water elevation for stations of east coast
NOAA stations from north to south.
Average correlation coefficient: 0.85
OBS
SCHISM
Notes: 1 min

## Slide 11
Model results: water elevation for stations of Northern Gulf of Mexico
NOAA stations from west to east.
Average correlation coefficient: 0.85
OBS
SCHISM

## Slide 12
Challenges: DEM issue
Low resolution of DEM leading to failure of resolving bathymetry
Station is located in a parking lot
5m
0m
CRM contours with 90m res.
SCHISM arcs
NOAA station
Mismatch of the DEM and imagery
NOAA station
NOAA station
0m
Solution: move the station towards deeper water when post-processing
Solution: no solution
Solution: no solution
Notes: 1 min

## Slide 13
Success: importance of resolving bathymetry
NOAA station 8656483 at Beaufort, NC
Channels are resolved to lead water transported to upstream.
Notes: 1 min

## Slide 14
Success: importance of resolving bathymetry
NOAA station 8449130 at Nantucket Island, MA
NOAA station 8447435 at
Chatham, Lydia Cove, MA
Arcs above 0m resolving the dry area.
Arcs below 0m resolving the wet area.
Notes: 1 min (can skip if out of time)

## Slide 15
Summary
During Hurricane Irene (2011), both storm and river induced surges are important
  The first surge is mostly from ocean but at stations away from the coast, compound flooding from rivers is also important
  Second and later surges are mostly due to river flooding; this is especially obvious at upstream stations
  Inflow from National Water Model is reasonably accurate for predicting compound surges
  Baroclinic adjustment is significant after the storm surge due to Gulf Stream adjustment
  The direct precipitation is important
We are applying the same technology to a 3D model for east coast + Gulf of Mexico
  SCHISM’s robust seamless capability enabled by polymorphism makes it efficient
  2D results show good model skills, provided that DEMs are accurate
  It’s important to resolve local features to capture the transformation of tides
Notes: 1 min