## Slide 1: Hydraulic Structures
Concepts and configuration
CALIFORNIA DEPARTMENT OF WATER RESOURCES
Eli Ateljevich, Bay Delta Office

## Slide 2: Types of structures
Transfers of (pumped) water
Weir
Culvert
Generic orifice equation
Radial Gate
  2 parameterizations
Weir/culvert combo

## Slide 3: Implementation
Common hydraulic/orifice equations
  Head difference assessed at reference nodes
  Prescribed flow (transfer) also possible
Similar implementation and restrictions as flux boundary
  Flows distributed uniformly over cross-section (1D)
  Required to not go dry locally
  Nudging factor is applied 0 < nu < 1
Structures can be “uninstalled” in time series
  Revert to normal hydrodynamics
Time series (th) multivariate, irregular

## Slide 4: Defining Structures
Reference nodes
“hydraulic head”
Paired nodes
Defined land-to-land
Structure
1
2
3
4
5
5’
4’
3’
2’
1’
Upstream
Downstream
Structure location
Reference node

## Slide 5: Steps Configuring the Structure
Prep mesh: node pairs, straight
Enable in param.in: ihydraulics=1
Geometry and parameters: hydraulics.in
Time series control: my_gate.th
See doc: Hydraulic Structures in SCHISM
******************************************
Preprocessor (BayDeltaSCHISM yaml-based system)
  Locations are physical (line segment)
  See preprocessor document or BayDeltaSCHISM examples

## Slide 6: Structure Time Series
#datetime install ndup op_down op_up elev width height
1999-11-26T08:24 1 2 1.0 1.0 -3.42 18.29 0
1999-12-14T09:24 1 2 1.0 1.0 -3.42 18.29 10
1999-12-14T14:25 1 2 1.0 1.0 -3.42 18.29 0
1999-12-15T09:22 1 2 1.0 1.0 -3.42 18.29 10
-4263060.0 1 2 1.0 1.0 -3.42 18.29 0
8762400.0 1 2 1.0 1.0 -3.42 18.29 10
9113400.0 1 2 1.0 1.0 -3.42 18.29 0
9368640.0 1 2 1.0 1.0 -3.42 18.29 10
install = 0 reverts to normal hydrodynamics
Series are multivariate
  Columns needed vary
  Documented in manual
Series are irregular
  Entry at 0. or negative required
BayDeltaSCHISM model_time.py to_elapsed utility used for translation

## Slide 7: Piers and Drag-inducing Structures
Drag forces formulas reasonable parameterization
Emergent SAV uses same assumption:
  Define large height to make emergent
  Density and diameter for A (area)

## Slide 8: Questions?
Eli.Ateljevich@water.ca.gov

## Slide 9: Follow us on social media
CADWR
cadepartmentofwaterresources
CA_DWR
calwater
Notes: NEGATIVE SPACE
GOOD