## Slide 1
Sediment dynamics modeling with SCHISM
SCHISM Workshop -- April 2019 -- Sacramento
MENGUAL Baptiste (baptiste.mengual@univ-lr.fr)

## Slide 2
Dynamics of sediments in marine environments
(from Wang and Adutta, 2013)
Focus on sand dynamics (suspended and bedload transport)

## Slide 3
SED2D
Based on semi empirical transport formula for suspension and bedload transport
Advection/diffusion not resolved
Only for non-cohesive sediments (sand and gravel)
Fast computation time
Solving both bedload and suspended dynamics  advection/diffusion equation
TVD scheme for tracer advection
Two types of sediment considered: non-cohesive (susp & bedload) and cohesive (susp only)
More time-consuming
For the two models:
Multi-layer/multi-class modules
Benefit of recent improvements in terms of numerical stability  Euler-Weno scheme
to solve Exner equation
2 sediment modules
SED3D
(Pinto et al., 2012)
(Fortunato and Oliveira, 2004, 2007; Dodet, 2013; Guérin, 2016)

## Slide 4
OUTLINE
Forcing / key processes
Sediment transport
Seabed compartment
SED2D/SED3D specificities
Applications / Ongoing studies
Perspectives & Conclusions

## Slide 5
Bottom shear stress
Current
limiters (drag coefficient)
]
Sediment: - diameter D
- : skin [ or form (ripples) roughness
Min in SCHISM
Max in SED2D
Min/Max values in SED3D
Water
column
Bottom layer
thickness
h
Initiation of motion  Forcing

## Slide 6
: Orbital velocity
: Wave friction factor
=f()
Many formulations
Swart (1974)
Nielsen (1992)
Soulsby (1997)
(relative bottom orbital excusion)
from Soulsby (1997)
(Jonsson, 1966)
Bottom shear stress
Waves
Initiation of motion  Forcing

## Slide 7
from Soulsby et al. (1993), Coastal Engineering
Current
Waves
Total
Bottom shear stress
Combined waves and current
Initiation of motion  Forcing

## Slide 8
Critical shear stress [N.m-2]
=
Mobility parameter [-]
Dimensionless grain size
from Soulsby (1997)
No motion
Sediment in motion if
Critical shear stress
Initiation of motion  Threshold

## Slide 9
Hydrodynamics: Bedform predictor  Form roughness sent back to SCHISM for estimates
Roughness length in sediment module: skin () or form ()
Ripples
Dunes
Sandwaves
Current
If
(e.g. Van Rijn, 1984)
Roughness length
If
Waves
Grant and Madsen (1982)
Nielsen (1992)
Total form roughness
Sediment-transport
component
Skin roughness

## Slide 10
Apparent roughness length due to the presence of waves
Roughness length
Shallow waters
waves affect (increase) in the wave bottom boundary layer
replaced by
e.g. Grant and Madsen (1979)
Wave boundary layer thickness 
re-estimated iteratively

## Slide 11
Sediment transport: case of SED2D
Suspended () and bedload () fluxes based on semi empirical formulations
Engelund and Hansen (1967)
Ackers and White (1973)
Soulsby-Van Rijn (1997)
Van Rijn (2007)
Camenen and Larson (2005, 2008)
Wu and Lin (2014)
Total sediment transport
Exner equation
[CL]
[WL]
CL and WL  more sophisticated, e.g:
Asymmetric wave velocity
Angle difference between waves and current
WL: hindering/exposure mechanisms in critical shear stress estimates
+ Possibility to account for bed slope effects (Lesser et al., 2004)

## Slide 12
Erosion/deposition fluxes
!- BOTTOM BOUNDARY CONDITION OPTION
!- 1 = Warner (2008)
!- 2 = Tsinghua Univ group (under dev)
!------------------------------------------------------------------------------
ised_bc_bot == 1
Sediment transport with SED3D: I. Suspension
Advection-diffusion equation
Horizontal
advection
Vertical
advection
Turbulent mixing
Vertical diffusion
Settling
Horizontal
diffusion
For each sediment class
Temporal evolution
of suspended concentration
Erosion
Deposition
Erosion
Deposition flux
Settling velocity []
Flux []
Erosion rate (same unit)
Class fraction [-]
Bed porosity [-]
(Partheniades, 1965)
(Soulsby, 1997)
Flux []
Bottom computational cell
prism
Eroded mass during limited by active
layer thickness (Harris and Wiberg, 1997)

## Slide 13
Erosion/deposition fluxes
!- BOTTOM BOUNDARY CONDITION OPTION
!- 1 = Warner (2008)
!- 2 = Tsinghua Univ group (under dev)
!------------------------------------------------------------------------------
ised_bc_bot == 1
Vertical
advection
Turbulent mixing
Vertical diffusion
Settling
Horizontal
diffusion
For each sediment class
Temporal evolution
of suspended concentration
Erosion
Deposition
New tracer advection scheme: TVD2
prism
FVM formulation with 3 sub-steps
1- Horizontal advection
2- Vertical advection
vertical level
index
Sub-time step
for CFL crit
Implicit  remove constraints due to high
3- Remaining terms
Sediment transport with SED3D: I. Suspension
Advection-diffusion equation
Horizontal
advection

## Slide 14
Bedload flux () based on semi empirical formulations
Soulsby and Damgaard (2005)
Van Rijn (2007)
Wu and Lin (2014)
[SD]
[WL]
Bed slope effect (Lesser et al., 2004)
Fluxes modulated depending on longitudinal
and transversal slopes
(from Soulsby, 1997)
Asymmetric waves (Elfrink et al.,
2006)
Angle between waves/current
accounts for
SD &
WL
(from Wu and Lin, 2014)
Sediment transport with SED3D: II. Bedload

## Slide 15
Exner equation
Basic method
Node-centered control volume with constant sediment flux
inside each element
Numerical oscillations
Conditions : Δt = 2 s ; Δx = 0.15 m (CFL<1) ; Qx = 0.001.u3
Sediment transport with SED3D: II. Bedload  Bed changes
(Guérin et al., 2016)

## Slide 16
Exner equation
Basic method
Node-centered control volume with constant sediment flux
inside each element
Adding artificial diffusion in transport :
Conditions : Δt = 2 s ; Δx = 0.15 m (CFL<1) ; Qx = 0.001.u3
Bathymetric filter
 drawbacks: methods based on arbitrary thresholds
Sediment transport with SED3D: II. Bedload  Bed changes
(Guérin et al., 2016)

## Slide 17
Finite volume formulation
New numerical scheme to solve the Exner equation
Main characteristic of the new scheme:
Q(x) is interpolated along Γi following a WENO method (Liu et al., 1994)
(Weighted Essentially Non-Oscillatory)
Q(x) is replaced by:
Sediment transport with SED3D: II. Bedload  Bed changes

## Slide 18
New numerical scheme to solve the Exner equation
Qx,1
Qx,2
Qx,3
Main characteristic of the new scheme:
Q(x) is interpolated along Γi following a WENO method (Liu et al., 1994)
(Weighted Essentially Non-Oscillatory)
Q(x) is replaced by:
 Exner finally resolved using Jacobian Conjugate Gradient method
Sediment transport with SED3D: II. Bedload  Bed changes
Weight
Stencil m
Polynomial
Oscillating
Indicator

## Slide 19
New numerical scheme to solve the Exner equation
Conditions : Δt = 2 s ; Δx = 0.15 m (CFL<1) ; Qx = 0.001.u3
Higher accuracy without additional diffusion or bathymetric filter
Sediment transport with SED3D: II. Bedload  Bed changes
(Guérin et al., 2016)

## Slide 20
Grid
Zoom on mouth
Conditions : Δt = 30 s ; Δx = 25 - 300 m (CFL<1) ; d50 = 0.5 mm ; Q following van Rijn (2007)
Tide:
M2 constituant
Waves:
Hs = 1.5 m
Tp = 10 s
Dirmoy = N290°
Morphodynamic application using SED2D: idealized inlet test case
Improvement due to the WENO scheme
(Guérin et al., 2016)

## Slide 21
Old scheme
(with diffusion et filter)
WENO method
Improvement due to the WENO scheme
Morphodynamic application using SED2D: idealized inlet test case
bathymetry
(Guérin et al., 2016)

## Slide 22
WENO method
Maumusson mouth
(Charente-Maritime, France)
1
2
Typical flood secondary channel (Bertin et al., 2009)
Morphodynamic application using SED2D: idealized inlet test case
bathymetry
Improvement due to the WENO scheme
(Guérin et al., 2016)

## Slide 23
WENO method
Figure from Hayes (1980)
2
Average migration rate ≈ 1.5 à 3 m/day (consistent with Pianca et al., 2014)
Morphodynamic application using SED2D: idealized inlet test case
bathymetry
Improvement due to the WENO scheme
(Guérin et al., 2016)

## Slide 24
Old scheme
(with diffusion and filter)
WENO method
Adjacent beach
evolution
Morphodynamic application using SED2D: idealized inlet test case
bathymetry
Improvement due to the WENO scheme
(Guérin et al., 2016)

## Slide 25
Adjacent beach
evolution
WENO method
Cap Ferret (Gironde)
Wavelength ≈ 350 to 500 m (consistent with Castelle et al., 2007)
Morphodynamic application using SED2D: idealized inlet test case
bathymetry
Improvement due to the WENO scheme
(Guérin et al., 2016)

## Slide 26
Variables describing bed properties in SED3D (each element)
All layers
Water
column
Layer
Sediment
compartment
Surficial layer only ()  Mean properties over all sediment classes
Managing bed compartment  SED3D
Fraction of each class
Mass of each class
Many other variables are defined at nodes, but only for coupling or output purposes
Thickness, age and porosity

## Slide 27
Update of sediment layer characteristics
Water
column
Layer
Sediment
compartment
Managing bed compartment  SED3D
Nbed layers always conserved
Case 1: Residual erosion
Merging surficial layers until satisfying
active layer criterion
Split bottom layer to keep Nbed layers
Case 2: Residual deposition
Create new layer if surf. lay. > user defined thickness
Mixing surficial layers until satisfying
active layer criterion
Combine/Split bottom layer to keep Nbed layers
bedload transport
vertical exchanges at water/sediment interface
following
 bathymetry update according to bed thickness changes
Morphodynamic coupling  morphological factor can be applied
(Warner et al., 2008)

## Slide 28
Managing bed compartment  SED2D
Surficial
layer
Sub-surface
layer
diameter of class i
50th-percentile diameter of class i
90th-percentile diameter of class i
Fraction of class i
N layers always conserved
Variables describing bed properties in SED2D
All layers (at each node)
At each node
Layer
Fixed parameters
Sub-surface layer thickness  VARIABLE
Thickness change linked to class i during a time step ()
Total thickness change during
Surface layer thickness  CONSTANT
<  Layers 2 & 3 merged, layer N split
>  Layer 2 split and bottom layers merged

## Slide 29
Managing bed compartment  SED2D
Fraction of class i in layer k
Surface layer thickness  CONSTANT
Sub-surface layer thickness  VARIABLE
Thickness change linked to class i during a time step ()
Total thickness change during
Surficial
layer
Sub-surface
layer
N layers always conserved
Update of sediment layer characteristics (following transport)
Layer
 erosion
 deposition
Sediment fractions
Thickness: only
Deposition case
update in k=1 and 2
Erosion case
update in k=1 only
(Reniers et al., 2013)

## Slide 30
Applications / Ongoing studies

## Slide 31
Available test cases for sediment dynamics (http://columbia.vims.edu/schism/schism_verification_tests/)
(Test_SED_Trench_Migration/
Test_Sed2d_Trench_Migration/)
Morphological development of riverine meander (Test_SED_meander_2/)
5 sediment classes
Elevation boundary condition only
Lateral migration enabled by
sediment avalanching
After 50 days
Initial time
Trench migration under a constant current
After 15 h
dx=0.1m dt=0.1s

## Slide 32
Morphodynamic application: idealized inlet test case
Ongoing work with SED3D
Bedload + Advection/diffusion for suspended sediment transport
3D circulation with wave/current interactions
d50=0.5mm (1 class)
MF=6
10 -levels
Waves: Hs=1.5m / Tp=10s
Z [m]
A
B
Sandbar formation
Initial profile
Final profile
A
B

## Slide 33
Bedload transport caused by wave acceleration
Sandbar migration due to wave non-linearity
Hoefel and Elgar (Science, 2003)
Model accounting for fluid accelerations in waves  Application at Duck Beach (North Carolina, USA)
Bedload term
Onshore migration reproduced
during mild wave conditions

## Slide 34
Sandbar migration due to wave non-linearity
Observed beach profiles
Model without
Model with
Bedload transport caused by wave acceleration
Setup of a configuration for Duck Beach
(realistic)
Implementation of term in SED3D
(formalism of Dubarbier et al., 2015)
Importance of
for 3D morphodynamic application
A
B
A
B
21 Sep
24 Sep
30 Sep

## Slide 35
Future developments / Perspectives

## Slide 36
Porosity of non-cohesive sediment mixtures
Geometric standard deviation (Cui et al., 1996)
Wooster et al. (2008)
Geometric standard deviation
Gravel (%) 8 mm
= 2-φ
Future developments: Bed compartment
Example with 1 gravel
and 2 sands
Influence on bed layer
thickness
diameter of sediment class [mm]
fraction of sediment class [-]

## Slide 37
Bed armouring
Future developments: Bed compartment
Garcia and Parker (1991)  Modulation of erosion rates for class i depending on mixture heterogeneity
Protection of underlying sediments by surficial coarser particles
with
Standard deviation of sediment distribution

## Slide 38
Cohesive sediments and sand/mud mixtures
Future developments: Bed compartment / Water-sediment interface
Accounting for consolidation (Grasso et al., 2015)
Including porosity modulation by cohesive sediments
(Wu and Li, 2017)
Time
Z
C
(from Grasso et al., 2015)
Sediment concentration
Mud fraction
Relative mud
concentration [kg/m3]
φ1
φ2
1 sand: D1 = 280 µm, = 0.4
1 mud: D2 = 2 µm, different
Porosity
Influence on critical shear stress for erosion

## Slide 39
Future developments: Bed compartment / Water-sediment interface
Interaction with non-cohesive sediments
Change in erosion behaviour of non-cohesive
sediments trapped in cohesive matrix ()
(from Le Hir et al., 2011)
consolidation
proxy
Mud fraction
Cohesive sediments and sand/mud mixtures
Critical mud fractions concept
No interactions
Transitional behaviour
 Interactions start
Independent
and
for each class
Pure mud behaviour (sand matrix trapped)
Sediment eroded as a mixture
and = f(mud fraction)
Same for all classes

## Slide 40
Future developments
Towards a fusion of the two sediment modules ?
Computation times for advection/diffusion of sediments strong increase/class added
Specific time step for advection/diffusion?
Gathering key concepts from each module

## Slide 41
Conclusions
2 sediment modules with different advantages/drawbacks
SED2D
Total transport
 semi empirical
Fast computation times
SED3D
Transport more sophisticated
 bedload + advection/diffusion
Time-consuming
SCHISM+WWM+SED3D: exciting perspectives dealing with morphodynamics!
Future improvements:
Bed compartment / Water-sediment exchanges (processes, sediment interactions)
Computation times